## Slide 1: TCP congestion control
Devyani tushar REMULKAR [2203110]
RUPESH HEMANT BHUSARE [2203106]
MARYADA HARSHINI [2203118]
MUDADLA SAI PRASANNA [2203120]

## Slide 2: What is Congestion?
Congestion is when a place or thing is
too crowded or full.
In network system:
Congestion occurs when network resources are overloaded.
Leading to delays, packet loss, and reduced throughput.

## Slide 3: THE PROBLEM
  How do we overcome this?
Problem is
  TCP Congestion Control Algorithm
Through:

## Slide 4: To overcome this:
The approach taken by TCP is, to have each sender limit the rate at which it sends traffic into its connection.
If a TCP sender perceives that there is little congestion on the path, then the TCP sender increases its send rate; if the sender perceives that there is congestion along the path, then the sender reduces its send rate

## Slide 5: Dynamically Adjusting Sending Rate
Changing network conditions in real-time.
This ensures efficient utilization of available bandwidth while preventing
network congestion.
Each side of a TCP connection consists: receive buffer, send buffer, and
several variables (like LastByteRead, cwnd, rwnd, etc.).

## Slide 6: Dynamically Adjusting Sending Rate
Congestion window(cwnd):
It refers to the amount of data that a sender can transmit to a receiver without receiving an acknowledgment (ACK) from the receiver.
Receiver window(rwnd):
  It’s a variable that indicates the amount of data that the receiver can
  accept at the current time
Unacknowledged data min(cwnd, rwnd)
It ensures that the sender doesn't send more data than either the cwnd or the rwnd can handle.

## Slide 7: Key Mechanisms for congestion control
Congestion Window Management: By adjusting cwnd based on perceived congestion, TCP regulates the sending rate to prevent overloading the network.
Detection of Congestion: TCP detects congestion through loss events, such as timeouts or receipt of multiple duplicate ACKs. These events signal network congestion, prompting TCP to adjust its transmission behavior accordingly.
Self-Clocking and Bandwidth Probing: TCP dynamically adjusts its transmission rate based on implicit signals from the network. It increases the rate until a loss event occurs, then backs off, effectively probing for the maximum sustainable rate without causing congestion collapse.

## Slide 8: TCP Congestion Control Algorithm

## Slide 9
The algorithm has three major components:
(1) slow start
(2) congestion avoidance
(3) fast recovery
celebrated TCP congestion-control algorithm. First described in [Jacobson 1988] and standardized in [RFC 5681].

## Slide 10: Slow Start
Linear additive increase takes too long to ramp up a new TCP connection from cold start.
Beginning with TCP Tahoe, the slow start mechanism was added to provide an initial exponential increase in the size of cwnd.
Remember mechanism by: slow start prevents a slow start. Moreover, slow start is slower than sending a full advertised window’s worth of packets all at once.

## Slide 11: Slow Start
cwnd initialized to a small value of 1 MSS
cwnd = cwnd+1 MSS for each of the acknowledged segments

## Slide 12: Figure: Slow Start
Source
Destination
Slow Start
Add one packet
per ACK

## Slide 13
  When should this exponential growth end?
Question:

## Slide 14
Loss Event
If there is a loss event (i.e., congestion) indicated by a timeout
ssthresh= cwnd/2
cwnd = 1 MSS
(shorthand for “slow start threshold”) when congestion was detected and begins the slow start process anew
ssthresh value
  When cwnd=ssthresh , slow start ends and TCP transitions into congestion avoidance mode.
3 Duplicate ACKS
  TCP performs a fast retransmit and enters the fast recovery state (we will see later)
Various Cases for SLOW START

## Slide 15: Congestion Avoidance
increases the value of cwnd by just a single MSS every RTT
Which implies cwnd = cwnd+ MSS/ cwnd bytes whenever a new acknowledgment arrives.

## Slide 16
When should congestion avoidance’s linear increase (of 1 MSS per RTT) end?
Question:

## Slide 17
When a timeout occurs - As in the case of slow start: The value of cwnd is set to 1 MSS, and the value of ssthresh is updated to half the value of cwnd when the loss event occurred.
A loss event also can be triggered by a triple duplicate ACK event. TCP halves the value of cwnd (adding in 3 MSS for good measure to account for the triple duplicate ACKs received) and records the value of ssthresh to be half the value of cwnd when the triple duplicate ACKs were received. The fast-recovery state is then entered.
3 dup ACKs indicates network capable of delivering some segments
timeout before 3 dup ACKs is “more alarming”
Philosophy:

## Slide 18: One Final Phase: Fast Recovery
The problem : congestion avoidance too slow in recovering from an isolated loss

## Slide 19: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped
  What ACKs do they generate?
  And how does the sender respond?

## Slide 20: Timeline
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 (no xmit)
ACK 101 (due to 106) cwnd=5 (no xmit)
ACK 101 (due to 107) cwnd=5 (no xmit)
ACK 101 (due to 108) cwnd=5 (no xmit)
ACK 101 (due to 109) cwnd=5 (no xmit)
ACK 101 (due to 110) cwnd=5 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so no ACKs for another RTT

## Slide 21: Solution: Fast Recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = cwnd/2
  cwnd = ssthresh + 3
While in fast recovery
  cwnd = cwnd + 1 for each additional duplicate ACK
Exit fast recovery new ACK
  Set cwnd = ssthresh

## Slide 22: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 23: Timeline
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
REXMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight (and now sending 115)
ACK 112 (due to 111) cwnd = 5 + 1/5  back in congestion avoidance

## Slide 25: TCP Flavors and TCP Fairness

## Slide 26: TCP FLAVORS
TCP-Tahoe – SS + AI + FastRetransmit
  ssthresh = cwnd/2 in FastRetransmit state
  cwnd =1 on both triple dupACK and timeout
TCP-Reno – SS + AI + FastRetransmit + FastRecovery
  cwnd =1 on timeout
  cwnd = cwnd/2 on triple dupack
TCP-NewReno – Reno + PartialAck
  TCP-Reno + improved fast recovery
TCP-SACK – Reno + Selective Ack
  incorporates selective acknowledgements

## Slide 27: TCP Tahoe vs. TCP Reno
Two similar versions of TCP
  TCP Tahoe (SIGCOMM’88 paper)
  TCP Reno (1990)
TCP Tahoe
  Always repeat slow start after a loss
  Assign slow-start threshold to half of congestion window
TCP Reno
  Repeat slow start after timeout-based loss
  Divide congestion window in half after triple dup ACK

## Slide 28
Conclusion:TCP Reno is better than TCP Tahoe as TCP Reno provides Fast Recovery

## Slide 29
Two goals of congestion control:
Fairness
Efficiency
Fairness : Every sender needs to gets their fair share
Efficiency : Network resources are used well

## Slide 30: TCP fairness
Fairness goal : If K TCP sessions share same bottleneck link of bandwidth R, each connection should have average transmission rate of R/K.
Achieving this goal, each connection gets an equal share of the link bandwidth

## Slide 31
Question:
Is TCP’s AIMD algorithm fair?

## Slide 32
Why?
As throughput increases, additive​
increase typically results in a slope ​of 1 ​
Multiplicative decrease decrease​
throughput proportionally​
R
R
equal bandwidth share
Connection 1 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
Connection 2 throughput
Full Bandwidth utilization line

## Slide 33
TCP THROUGHPUT

## Slide 34
What’s the average throughput of TCP as a function of window size and RTT?
Question:

## Slide 35: Calculation on a simple model
Ignore slow start
Let W be the window size (cwnd) (measured in bytes) when loss occur
  Loss is detected by duplicate ACKs
Window: …
  Increase the window size by 1 MSS for each RTT until a loss event occurs at W
  After W/2 RTTs, loss event occurs then drop the window to half and repeat

## Slide 36: Calculation on a simple model
When window is W, throughput is W/RTT
Just after the loss , window drops to W/2 ,throughput to W/2RTT
Assuming that RTT and W are approximately constant over the duration of the connection, the TCP transmission rate ranges from W/(2 · RTT) to W/RTT
Average throughput: 0.75W(MSS/RTT)
  Avg of W packets per RTTs and there are RTTs between two packet drops
  i.e, One packet is dropped out of ()*() = ()W2 packets

## Slide 37: TCP Throughput/loss Relationship
Packet drop rate, p = W-2
W = (p)-2
Throughput = (MSS/RTT) = ()*(p)-2 (MSS/RTT)
= (p)-2(MSS/RTT)
Throughput= (MSS/RTT)
Flows get throughput inversely proportional to RTT and packet loss

## Slide 38: A Simple Model for TCP Throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 39: A Simple Model for TCP Throughput
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs
A=(3/8)W2

## Slide 40: OtheR alternatives

## Slide 41: Control System Model
(Fairness)
= 1 (Efficient)
> (Congestion)

## Slide 42: Four alternatives
MIAD: Multiplicative increase, Additive decrease
  aI=0, bI>1, aD<0, bD=1
AIAD: Additive increase, Additive decrease
  aI>0, bI=1, aD<0, bD=1
MIMD: Multiplicative increase and Multiplicative decrease
  aI=0, bI>1, aD=0, 0< bD<1
AIMD: Additive increase, Multiplicative decrease
  aI>0, bI=1, aD=0, 0<bD<1
Simplest control strategy by Chiu and Jain(1988)

## Slide 43: Multiplicative Increase, Additive Decrease(MIAD)
aI=0, bI>1, aD<0, bD=1
quickly reach high bandwidth
utilization.
Increasing the sending rate
multiplicatively
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
congested 
 inefficient
(, )
(x1+aD,x2+aD)

## Slide 44: Additive Increase, Additive Decrease(AIAD)
aI>0, bI=1, aD<0, bD=1
Efficiency is somewhat lower
compared to MIAD.
Increase in sending rate is
additive.
Slower convergence to high
bandwidth utilization.
fairness
line
User 1: x1
User 2: x2
(x1,x2)
(x1-aD,x2-aD)
(x1-aD+aI),x2-aD+aI))
congested 
 inefficient

## Slide 45: Multiplicative Increase, Multiplicative Decrease(MIMD)
aI=0, bI>1, aD=0, 0<bD<1
Efficiency is well-maintained.
Aggressively increasing sending
rates and proportionally reducing
them upon congestion
User 1: x1
User 2: x2
fairness
line
(x1,x2)
(bdx1,bdx2)
(bIbDx1,bIbDx2)
congested 
 inefficient

## Slide 46: Additive Increase, Multiplicative Decrease(AIMD)
aI>0, bI=1, aD=0, 0<bD<1
Efficiency may be compromised
due to additive increase.
Well suited where fairness is
primary concern.
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,
bDx2)
congested 
 inefficient

## Slide 47
MIMD
AIAD
MIAD
AIMD
Images Taken from the slides of CS390: lec8-9
Stable!
But doesn’t converges to Fairness
Unstable!
Goes away from Fairness
Converges to stable and fair cycle
Symmetric to fairness

## Slide 48: A Critical Analysis of TCP CC

## Slide 49: Failings of TCP Congestion Control
Leads to the Queuing of packets(large delays)
Does not scale to high-speed
Produces irregular saw-tooth behaviour
Takes a long time to reach steady state
Depends on RTT(unfair)
Depends on losses(non congestive losses)

## Slide 50
DEMO

## Slide 51: Four alternatives
MIAD: Multiplicative increase, Additive decrease
  aI=0, bI>1, aD<0, bD=1
AIAD: Additive increase, Additive decrease
  aI>0, bI=1, aD<0, bD=1
MIMD: Multiplicative increase and Multiplicative decrease
  aI=0, bI>1, aD=0, 0< bD<1
AIMD: Additive increase, Multiplicative decrease
  aI>0, bI=1, aD=0, 0<bD<1
Simplest control strategy by Chiu and Jain(1988)

## Slide 52
MIAD
AIAD
SIMULATION RESULTS
  aI=0, bI=1.125, aD=-3, bD=1
  aI=1, bI=1, aD=-3, bD=1

## Slide 53
MIMD
AIMD
SIMULATION RESULTS
  aI=0, bI=1.125, aD=0, bD=0.8
  aI=1, bI=1, aD=0, bD=0.8

## Slide 54: Quiz

## Slide 55: REFERENCES
https://www.ucg.ac.me/skladiste/blog_44233/objava_64433/fajlovi/Computer%20Networking%20_%20A%20Top%20Down%20Approach,%207th,%20converted.pdf
https://slideplayer.com/slide/6466058/#google_vignette
https://miet.ac.in/assets/uploads/cs/TCP.pdf
https://www.researchgate.net/publication/2937689
https://slideplayer.com/amp/8694372/
https://www.slideserve.com/lovey/congestion-control-and-active-queue-management
https://www.slideserve.com/pbenning/tcp-fairness-powerpoint-ppt-presentation

## Slide 56: THANK YOU